## Slide 1: MicroMegas Trigger Processor Implementation
Nathan Felt
2015 May 4

## Slide 2: ART Data/Trigger Processor Overview

## Slide 3: ADDC GBT Data Packet
Each ADDC will service 2 sets of 32 VMMs and have 2 fiber outputs using the GigaBit Transceiver (GBT) architecture. One fiber per 32 VMMs
The GBT packet in widebus mode will provide 112 data bits at a rate of 4.8 Gbs and arrives once every bunch crossing
  HIT_CNT = 4-bit number of hits (range 0 - 8; 9 - 15 invalid)
  ART_DATA = 6-bit triggered VMM strip number
  ARTDATA_PARITY = 8-bit parity, one per hit
  HIT_LIST= The triggered state of each of the 32 VMMs will be represented as a single bit in this 32-bit field.

## Slide 4: ADDC GBT Data Packet

## Slide 6: Implementation
320 MHz Internal Clock
1/16th sector slice, containing all elements of algorithm implemented
Modelsim used for simulation
Xilinx Vivado 14.4 used for synthesis and PAR
No timing errors in algorithm
Extrapolated resource estimate
  70% targeting a ‘485
  50% targeting a ‘690.
Source code on SVN

## Slide 7: Development Platform

## Slide 8: Development Platform
Matlab used for all data formatting, communication and analysis
Communication uses TCP/IP on Mircroblaze with AXI interface to Programmable Logic
ADDC Emulator
  Generates GBT packets from track data files
  Currently lives in Trigger Processor FPGA
GBT Loopback
  Option to bypass
  Implementation uses code from the CERN GBT-FPGA project

## Slide 9: Development Platform
Algorithm hardware results comparable to computer simulation
  Currently working on increasing the bit resolution of some variables, This will likely increase latency by 6 – 9 ns
Initial data communication with BNL ADDC verified

## Slide 10: Development Platform

## Slide 11: Ancillary functions
Ancillary functions common to both MM and sTGC can be shared as well-defined packages.
Ancillary functions Include
  Timing and Trigger control (TTC)
  Level-1 pipeline and derandomizer
  read/write of configuration parameters
  monitoring
  playback for debugging
  Segment output to Sector Logic
  Segment output to “other” detector’s trigger processor
Three groups will participate in writing the firmware:
  Harvard
  Illinois
  Weizmann

## Slide 13: Backup

## Slide 14: Hardware / Software Example Comparisons

## Slide 15: Trigger Processor with ADDC

## Slide 16: Monitoring Functions

## Slide 17: Data Path