## Slide 2: LAr System Block Diagram

## Slide 3: AMC Features
48 Optical Rx/Tx channels
  32 Rx channels required for ART data from Art Data Driver Cards (GBT link)
  Avago Micropod connection on front panel
Xilinx Virtex 7 (XC7VX485T-2FFG1927C)
  Same FPGA used in the current Trigger Processor firmware development (VC707)
  Algorithim estimate is 70% of “485”
  Pin compatible w/550, 690
Two LVDS Tx/Rx signals
  Can be configured as four Tx or four Rx signals
  Looking into expanding this to eight LVDS connections
  Can be used for a low latency lateral communication between AMC boards

## Slide 4: Merging
LVDS connections can provide the lateral communication between AMC cards needed for sTGC and MM merging
Lowest latency trigger processor, MM or sTGC, will send its data to the other and the merged data will be sent from a single AMC.

## Slide 5: Features
Carrier
  Four AMC slots
  AMC connections are identical on each slot

## Slide 6
Hardware iterations and