Hits from GBT
- 120 bit GBT packet length
- @4.8 Gb/s, 25 ns Tx length, 1 GBT packet/BC
- 4 X MMFE-8/GBT = 32 VMM/GBT
- 1 Trigger Processor AMC per 32 GBT (1 wedge)
- A number of multipliers can be assigned to each GBT link to convert strip addresses to slope in parallel
- Each Finder region needs to look at the new slopes from 2 GBT links, select the appropriate hits and store.

---
Slope Calculation and Binning
Finder Region
Binning
2 ticks
3 ticks
Addr to Slope
Addr to Slope
GBT
Addr to Slope
Addr to Slope
Addr to Slope
Addr to Slope
GBT
Addr to Slope
Addr to Slope
Addr to Slope
Addr to Slope
GBT
Addr to Slope
Addr to Slope
Addr to Slope
Addr to Slope
GBT
Addr to Slope
Addr to Slope
...

---
Number of Hits per GBT Packet
# Hits / GBT Packet	Inner GBT	Outer Gbt
0 to 1	56.6%	97.0
0 to 2	82.1%	99.7
0 to 3	94.3%	99.9
0 to 4	98.5%	100
0 to 5	99.7%	100
- Distribution function using John O occupancy spreadsheet and Treating hits as independent
- VMM borders and MMFE-8 stacked in z will increase hit count.