## Slide 1: NSW trigger concept



Phase I upgrade: Increased backgrounds, but must maintain existing trigger rate
Filter “Big Wheel” muon candidates to remove tracks that are not from the IP
Only track “A” should be a trigger candidate: pointing:  < 7.5mrad
Challenge is latency: 500nsec for electronics + 500ns fibres to be in time for Big Wheel
Micromegas: 2M strips, 0.4mm
sTGC: 280K strips (3.2mm), 45K pads, 28K wires
sTGC, MM find candidates
independently,
list merged for Sector Logic
Hit per layer: sTGC:
hit is centroid of 3-5 strips
Micromegas:
hit is address of strip